Provided by www.YuvaJobs.com - SNDT mumbai ,28 June 2009

RINL Visakhapatnam steel Plant

Hi,

I went through RINL paper in mechanical stream. There were 70 techanical+80aptitute questions total time was 2.5 hours. times was more than sufficient. I finished my paper within 2 hours. questions in technical section was from strength of materials, springs, rivet joints,2 question from welding. nearly 50 question out 70 were from first two chapter of KHURMI-GUPTA objective mechanical.

1) Spring in clutch & brake is used for

a)apply force b) absorbing shock c) power transmission d)none

2) In spring force per unit deflection is known as

ans) spring stiffness

3) For shock absorbing which spring is used

a)closed coil helical spring b) open coil helical spring c)leaf spring d)none

4) Change in length to original length is known as

Ans) strai

5) What is resilience

6) Energy stored in a body due to its position is known as

Ans) potential energy

7) Force applied on a body can cause

a) retardation in body b) internal stress c) d)all

8) Suddenly applied load is_______times gradual applied loads.

Ans) Two times

9) Hoop stress is_____________times longitudinal stress.

10) Design of thin pressure vessel is based on

a) Hoop stress

b) Longitudinal stress

c) Geometric mean of hoop and longitudinal stress.

d) Arithmatic mean of hoop and longitudinal stress

11) What is slenderness ratio is

Ans) l/k

12) If slenderness ratio is less than 80 columan is known as

Ans) short column

13) Eulers formula holds good for

a)short column b) long column c) botn short and long d)none

14) Rankine formula holds good for

a)short column b) long column c) botn short and long d)none

15) Formula for change in length

Ans) PL/AE

16) Linear stress is to linear strain is known as

Ans) young`s modulus

17) Distance between two rivets in known as

Ans) pitch

18) Distance between center of hole and edge of plate is known as

Ans) Margin

19) Failure of rivet joint is take place by

a) shear b) crushing c) break of rivet on one side of plate d) all

20) In which welding process consumable electrode is used

Ans) MIG

21) Breaking stress is ___________than ultimate stress

Ans) less

22) Tensile test is perform of________

Ans) Ductile material

23) Compressive test is performed on________

Ans) Brittle material

24) In ductile material tensile strength is_______compressive strength.

a) less b) more c) equal d) not

25) Stress is directly proportion to strain upto__limit

Ans) Elastic limit.

26) Beyond elastic limit

a) strain increases faster than stress b) stress increases faster than strain c) both at equal rate d)

27) Unit of power

Ans) watt

28) In SI system unit of stress is

a) N/mm^2 b)kN/m^2 c) MN/m^2 d)all

29) Unit of work

Ans) N-m

30)1 Watt is equal to

Ans) 1 J/s

31) Efficiency of a machine is

a) output/input

b) work done by machine /work done on machine

c) mechanical advantage/velocity ratio

Ans) all

32) Lifting machine is

a) Reversible machine

b) Non reversible machine

c) Ideal machine

d) None

33) Finding resultant of forces is known as

Ans) Composiotion

33) Centroid is a point

a) Same as Center of gravity.

b) Where all the forces of resultant act

c)

d)

34) Moment of inertial of rod about center of gravity is to M.I. about one of its end is_____

35) Moment of inertia of a body is

a)second moment of mas

b)

c)

d)

APTITUTE SECTION

1) Meaning of flinth

2) Meaning of hypocrisy

3) Opposite of pseudo

4) 2008 man booker prizer winner

Ans) Arvind adiga

5) South african president zacob zuma is of which caste?

some questions were on maths,data interpretation,fill in the blanks with correct words,odd man out,series etc.

Provided by www.YuvaJobs.com - SNDT mumbai ,28 June 2009